## Slide 1: Network voltage management
Network voltage management refers to the process of regulating and maintaining a stable voltage level within an electrical power network.
Voltage management is critical to ensuring the safe and efficient operation of electrical equipment and preventing damage to the power grid.
One of the primary goals of voltage management is to maintain the voltage level within a specified range, typically between 110V and 240V.
Voltage can fluctuate due to factors such as changes in demand, fluctuations in supply, and other external factors such as weather conditions.
Voltage management techniques aim to mitigate these fluctuations and maintain a stable voltage level within the specified range.
Overall, effective voltage management is critical to ensuring the safe and efficient operation of electrical networks, reducing downtime, and minimizing the risk of damage to equipment.

## Slide 2: Network voltage management
There are several techniques used in voltage management, including:
Load management:
  This involves adjusting the amount of load on the network to regulate voltage levels.
  Load management can be achieved by adjusting the voltage levels at the source, using voltage regulators, or by adjusting the amount of power supplied to individual loads.
Reactive power compensation:
  Reactive power compensation is defined as the management of reactive power to improve the performance of alternating-current (ac) power systems.
  In general, the problem of reactive power compensation is related to load and voltage support.
  Reactive power compensation involves the use of reactive power devices such as capacitors and inductors to manage voltage levels.
  These devices can be installed at various points in the network to maintain a stable voltage level.

## Slide 3: Network voltage management
Voltage regulation:
  Voltage regulation involves adjusting the voltage level at the source to ensure that it remains within the specified range.
  This can be achieved by using voltage regulators or transformers.
Power factor correction:
  Power factor correction involves improving the power factor of the network to reduce losses and improve efficiency.
  This can be achieved by installing capacitors or other reactive power devices.
  Power factor correction is the process of compensating for the lagging current by creating a leading current by connecting capacitors to the supply.
  A sufficient capacitance is connected so that the power factor is adjusted to be as close to unity as possible.

## Slide 4: Network voltage management
Power factor correction:
  cos θ = Power factor of the circuit i.e. phase difference between current and voltage waves.
  So, if we put cos 90° = 0, then the overall power of the circuit will be zero (i.e. In a pure Inductive circuit where voltage is leading by 90° from respectively). Ideal value of power factor is unity (cos θ=1) which enhances the efficiency of the system.
  Power factor compensation can be active or passive.
  Passive power factor correction involves the use of capacitors.
  Active power factor correction involves the adjustment of firing angle of devices like thyristor.

## Slide 5: Power Quality Management
Power quality management refers to the process of ensuring the quality of electrical power supplied to consumers.
It involves monitoring, controlling, and improving various aspects of power quality, including voltage level, frequency, harmonics, transients, and interruptions.
Poor power quality can cause problems such as equipment failure, production losses, and safety hazards.
Power quality management aims to minimize these problems and ensure the reliable and efficient operation of electrical systems.
Some common power quality management techniques include power factor correction, voltage regulation, harmonic filtering, surge suppression, and uninterruptible power supply (UPS) systems.
Power quality monitoring and analysis tools are also used to identify and diagnose power quality problems and implement appropriate solutions.

## Slide 6: Power Quality Management
Power quality management techniques can include:
  Power factor correction: This involves adjusting the ratio of active power to apparent power, which can improve the efficiency of electrical equipment and reduce energy costs.
  Voltage regulation: This involves regulating the voltage level to ensure that it remains within a certain range, which can prevent equipment damage and ensure proper operation.
  Harmonic filtering: This involves removing harmonics from the electrical signal, which can reduce the risk of equipment damage and improve power quality.
  Surge protection: This involves protecting equipment from voltage surges caused by lightning, switching operations, or other sources, which can cause equipment damage and downtime.
  Transient suppression: This involves suppressing transient voltage spikes, which can cause equipment damage and interfere with equipment operation.

## Slide 7: Frequency Management
Frequency management in the transmission and distribution of electrical energy is the process of maintaining the grid frequency (50 Hz or 60 Hz) within strict, safe, and operational limits by ensuring a continuous, real-time balance between power generation and consumption. When demand exceeds generation, the frequency drops; when generation exceeds demand, the frequency rises.
Frequency control is primarily managed at the transmission level by Transmission System Operators (TSOs) using, as of 2025, a combination of traditional spinning reserves and, increasingly, inverter-based resources.

## Slide 8: Frequency Management
Key Levels of Frequency Regulation
Frequency regulation is structured into three distinct control levels:
Primary Control (Frequency Containment Reserve - FCR): Mandatory, automatic response (within 15-30 seconds) by generator governors to stabilize the frequency following a deviation.
Secondary Control (Automatic Generation Control - AGC/aFRR): Automatic, centralized control that restores frequency to the nominal value (50/60 Hz) and balances interchange between control areas within 5 minutes.
Tertiary Control (Manual Regulation - mFRR): Manual, scheduled adjustment of generation to restore secondary reserves and manage network congestion, typically taking 15 minutes

## Slide 9: Frequency Management
Frequency Management in Transmission (High Voltage) TSOs use specialized tools to manage frequency, especially when dealing with high-voltage (220kV-400kV+) transmission.
Inertia Support: Synchronous generators provide rotational inertia, allowing the grid to resist sudden frequency changes.
Active Power Control: Adjusting the output of large-scale generators to match demand.
HVDC Links: High-Voltage DC (HVDC) links are used to connect asynchronous AC systems and allow rapid, precise control of power flow to stabilize frequency.
Congestion Management: Using "redispatch" to re-route power, often necessitated by renewable energy variability.

## Slide 10: Frequency Management
Frequency Management in Distribution (Medium/Low Voltage) Distribution System Operators (DSOs) are increasingly responsible for frequency, as 70% of new renewable energy is connected to distribution grids.
Distributed Energy Resources (DERs): Rooftop solar and home batteries are used for localized frequency support.
Virtual Power Plants (VPP): Aggregated DERs can provide frequency services similar to large plants.
Demand Response: Intelligently controlling demand (e.g., HVAC systems, EV charging) to increase or decrease consumption.
Virtual Inertia/Grid-Forming Inverters (GFM): Power electronics that mimic the behavior of rotating machines to add stability to low-inertia, renewable-dominated networks