## Slide 1: Influence of PV on System Transient Response
Inertia: PV systems typically do not have any inherent rotational inertia, which means they cannot provide the same level of stability and damping during grid disturbances as traditional synchronous generators. This lack of inertia can potentially lead to frequency deviations and voltage fluctuations during transient events.
Fault current contribution: PV systems can provide additional fault current to the system during transient events, which can help to improve the fault clearing performance of protection devices. However, this can also lead to overcurrent issues and may require additional protection measures to be implemented

## Slide 2: Influence of PV on System Transient Response
Voltage support: PV systems can provide voltage support during transient events by injecting reactive power into the system. This can help to stabilize the grid and improve voltage stability, particularly in weak areas of the system.
Control strategies: Advanced control strategies for PV systems, such as virtual inertia and fast frequency response, can help to mitigate some of the transient response issues associated with PV integration. These strategies can provide additional stability and damping during grid disturbances, similar to the way traditional generators operate

## Slide 3: Influence of WECS on System Transient Response
Voltage fluctuations: WECS can cause voltage fluctuations due to the intermittent nature of wind. These fluctuations can lead to transient instability in the system, especially if they are large in magnitude and frequency.
Reactive power support: WECS can provide additional sources of reactive power to the grid, which can improve the transient stability of the system. The power electronics used in WECS can be used to control the flow of reactive power into the grid, helping to maintain the voltage stability of the system

## Slide 4: Influence of PV / WECS on System Transient Response
Frequency deviations: WECS can cause frequency deviations in the power grid due to the variability of wind speed. These deviations can also lead to transient instability in the system, especially if they are large in magnitude and frequency.
Damping of oscillations: WECS can help to improve the damping of oscillations in the power grid. This is because the power electronics used in WECS can be used to actively control the output of the turbines, which can help to damp out any oscillations that occur in the system